# iocom design goals
X…

- Connect controller to distributed IO devices
- Open source, free to use also as part of commercial code.
- Documented (working on it) simple protocol to connect devices from different manufacturers.
- Code can be ported to any system with standard C compiler.
- Data is seen as memory blocks. Memory blocks are plain byte arrays.
- Memory blocks are transferred to one direction only.
- Application never locks up. If communication doesn’t keep up with changes by application, frames are dropped.
- Data transfer synchronization, so that application will know that whole data set is complete.
- Preserve order of changes.
- Low small transaction latency (typical goal 1-5 milliseconds depending on hardware).
- High throughout in bigger transactions.
- High limits for maximum address space size are high (8/16 bit micro-controllers typically 32k, linux/windows/etc about 2GB). Practical limits are set by available system memory.
- Point to point connection over TCP socket or full duplex serial communication.
- Low overhead. Small message headers, transfer only changes, compress transferred data.